FICSES usage
V_2.0
2019/08/10
Akram

---
Outline
- Perquisites
- Revisions
- High-level architecture
- FIC design modifications
- HLS modules
- Testing
- Remarks

---
Perquisites
- This document is based on:
  - :drive/FIC_DDR4_Feb22_2019.pdf
  - :drive/FICSES.pptx
- Please read carefully the above two documents before going any further

---
Revisions
- V_1.0
  - Initial version
- V_2.0
  - Change the connecting lane between FICSES and FIC boards from Lane3 to Lane5
  - Add FICSES support to MARK2 boards
  - Notes about HLS output to FICSES
  - FICSES control can be done using C programs (ficses.h) instead of shell scripts

---
High-level architecture
Transceiver
Firefly cable
FIC00
FIC01
FIC07
Lane0
Lane1
ZEUS
Lane2
…..
Lane3
FICSES
KUC1500
Lane4
Lane5
Lane6
Lane7
- FICSES is attached to ZEUS through PCIexpress.
- Two transceivers are available on FICSES. But only one is used at the moment.
- FICSES is connected to FIC00 via Lane5 through a Firefly cable.
- In FIC00 ~ FIC07, Lane6 and Lane7 are reserved for a ring network to transfer the data and control from/to ZEUS
- Lane0~Lane4 can be used for the user network

---
High-level architecture
- The lane used by FICSES to connect to FIC00 has four channels.
  As explained in “FICSES.pptx”, ZEUS writes a 512KB binary file to FICSES for each lane: 256KB write data + 256KB zeros (read space initialization).
- The received data in FICSES is first stored in a 512KB buffer (256bit x 16384).
  Then, only the the lowest 170 bit are forwarded to Aurora. Data[255:170] is discarded!
  The 170th bit must be “1” and it is used as the valid signal (Similar to FIC!).
- In a similar approach, ZEUS reads the entire 512KB FICSES buffer and store it to a binary file.
  The “Read Binary File” contains both the previously write data as well as the new data read from FICSES.
512KB
256bit x 16384 buffer
Write Binary File
Write Space
(256KB)
170bit
170 bit
512KB
Read Space
(256KB)
Read Binary File
170bit
170 bit
ZEUS
FIC00
FICSES
PCIe
Aurora (Lane3)
Aurora

---
High-level architecture:
Zeus --> FIC00
Write Binary File
256bit x 16384
Buffer
256bit x 16384
Received data
in func4x4
1
1
1
{86'h0,1'h1,169'h1}
{86'h0,1'h1,169'h1}
{1'h1,169'h1}
.
.
.
.
.
.
.
.
.
8192
{1'h1,169'hF}
8192
8192
{86'h0,1'h1,169'hF}
{86'h0,1'h1,169'hF}
8193
8193
{256'h0}
{256'h0}
.
.
.
.
.
.
.
.
.
.
.
.
16384
16384
{256'h0}
{256'h0}
ZEUS
FICSES
FIC00

---
High-level architecture:
FIC00 --> Zeus
Read Binary File
256bit x 16384
Buffer
256bit x 16384
Received data
in func4x4
1
1
1
{86'h0,1'h1,169'h1}
{86'h0,1'h1,169'h1}
{1'h1,169'h1}
.
.
.
.
.
.
.
.
.
8192
{1'h1,169'hF}
8192
8192
{86'h0,1'h1,169'hF}
{86'h0,1'h1,169'hF}
Sent data
from func4x4
{86'h0,1'h1,169'hA}
{86'h0,1'h1,169'hA}
8193
8193
1
{1'h1,169'hA}
.
.
.
.
.
.
.
.
.
16384
16384
8192
{1'h1,169'hB}
{86'h0,1'h1,169'hB}
{86'h0,1'h1,169'hB}
ZEUS
FICSES
FIC00

---
FIC design modification:
Top level
- To allow receiving/sending packets from/to ZEUS, a new module is added at the top_level:
  - In FIC00, the new module (ficses_ctrl.v) receives data/control from FICSES through Lane5, and either pass it to the local func4x4.v, or forward it to other FIC boards through Lane6.
  - In FIC01~07, ficses_ctrl.v receives data/control from other FIC boards through Lane6/7, and either pass it to the local func4x4.v, or forward it to other FIC boards through Lane6/7.
FIC00
FIC01
FIC07
fic_top.v
func4x4.v
func4x4.v
…..
func4x4.v
ficses_ctrl.v
ficses_ctrl.v
FICSES
Lane6
Lane6
Lane6
Lane5
ficses_ctrl.v
Lane7
Lane7
Lane7

---
FIC design modification:
Data/Control path
- When writing data (DDR or control reg) from ZEUS to FIC01~07, ficses_ctrl in FIC00 always forwards the write packet via Lane6.
- When reading data (DDR or control reg) from FIC01~07, this later should always make sure that the reply packet arrives to FIC00 via Lane7.
  - if(board_id[0] == 0) send reply through Lane6
  - if(board_id[0] == 1) send reply through Lane7
FIC00
(000)
FIC02
(010)
FIC04
(100)
FIC06
(110)
FIC01
(001)
FIC03
(011)
FIC05
(101)
FIC07
(111)
Lane6
Lane6
Lane6
Lane6
Lane6
Lane6
Lane6
Lane6
Lane7
Lane7
Lane7
Lane7
Lane7
Lane7
Lane7
Lane7

---
FIC design modification:
Channel partition
- Although each lane has 4 channels, in the current design only two channels are used in FICSES:
  - Channel 0 (unused)
  - Channel 1 (Control): dedicated for register access in func4x4
  - Channel 2 (Data): dedicated for DDR data access (write/read)
  - Channel 3 (unused)
FIC00
FIC01
func4x4.v
FICSES
Lane5
ficses_ctrl.v
Lane6
Lane6
Channel0
Channel0
Channel0
Channel0
Channel1
Channel1
Channel1
Channel1
Channel2
Channel2
Channel2
Channel2
Channel3
Channel3
Channel3
Channel3
from_ses_ctrl
from_ses_data
to_ses_ctrl
to_ses_data

---
FIC design modification:
Packet format
From ZEUS, users always send a 256bit packet. In FICSES, only 170bit are kept and transferred to FIC00 in the below format:
- Valid:
  - Should always be assigned to “1”; otherwise it will be dropped in FICSES
- Payload:
  - Data to be written to DDR or control reg
- Command:
  - 9'h1: ap_start
  - 9'h2: write
  - 9'h3: read
  - 9'h4: ap_reset
  - 9'h5: Routing table setting
Valid
1bit
Command
9bit
Dest_board
8bit
Src_board
8bit
Register Address
16bit
Payload
128bit

---
FIC design modification:
Packet format
- Dest_board:
  - Board ID to which ZEUS wants to write/read to/from.
  - The ID is represented by the Dip_switch value in the board.
  - When setting Dest_board to 0xBB, a write packet is broadcasted to all the boards connected in the ring network
    (Read broadcast is not supported at the moment!!)
- Src_board:
  - Board ID from which the data/control is coming from.
  - 0xFF represents ZEUS ID
Valid
1bit
Command
9bit
Dest_board
8bit
Src_board
8bit
Register Address
16bit
Payload
128bit

---
FIC design modification:
Packet format
- Register Address:
  - SES_STAT	16'hffff	// (R/W)	Status register
  - SES_TEST	16'hfffe	// (R)	Direct read/write to HLS module
  - SES_LUP	16'hfffd	// (R)	Link up
  - SES_DIPSW	16'hfffc	// (R)	Dipsw value
  - SES_LED	16'hfffb	// (R/W)	LED value.
  - SES_CHUP	16'hfffa	// (R)	Channel up
  - SES_TIMER	16'hfff9	// (R)	Timer
  - SES_SNUM	16'hfff8	// (R/W)	Slot number register
  - SES_PKT0_3	16'hfff7	// (R)	PKT monitor 0~3
  - SES_PKT4_7	16'hfff6	// (R)	PKT monitor 4~7
  - SES_SLOT	16'h2000	// (R/W)	Slot register
  - SES_DDR_WR_START	16'hDDD1	// (W)	For ddr_write_start HLS module
  - SES_DDR_RD_START	16'hDDD2	// (W)	For ddr_read_start HLS module
  - SES_DDR_ADDR	16'hDDDA	// (R/W)	DDR address
Valid
1bit
Command
9bit
Dest_board
8bit
Src_board
8bit
Register Address
16bit
Payload
128bit

---
HLS modules:
High-level view
fic_top.v
fucn4x4.v
AXI
Interconnect
AXI4
from_ses_data
128bit
S
HLS
ddr_write
MIG
Interface
ddr4_0
AXI4
M
ficses_ctrl.v
AXI4
HLS
ddr_read
S
to_ses_data
128bit
100 MHz
200 MHz

---
HLS modules:
DDR Access
- Two HLS modules are used in this design similar to “:drive/FIC_DDR4_Feb22_2019.pdf”
  - ddr_write: receives data from FICSES and write them to DDR
  - ddr_read: read from DDR and send them to FICSES
- In func4x4, Payload (128bit) is fetched from the 170bit from_ses_data packet coming from “ficses_ctrl” and fed to “ddr_write” HLS module
- Also, func4x4 adds the necessary fields to the read data (128bit) from the “ddr_write” HLS module and send it to “ficses_ctrl” as 170bit to_ses_data packet
  - Add the valid bit
  - Set the “Dest_board” to 0xFF (Zeus ID)
  - Set the “Src_board” to the board ID read from the Dip_switch

---
HLS modules:
ddr_write.c
#include "ap_cint.h"
#include "string.h"
#define MAXDATA 8192
void ddr_write (uint128 input[], volatile uint128 *ddr)
{
#pragma HLS INTERFACE m_axi port=ddr offset=direct max_write_burst_length=256
#pragma HLS INTERFACE axis port=input
int i;
uint128 buff_wr [MAXDATA];
 for (i = 0; i< MAXDATA; i++) {	// input from FICSES
 #pragma HLS PIPELINE
 buff_wr[i] = input[i];
 }
memcpy((uint128*)ddr, buff_wr, MAXDATA*sizeof(uint128));
return;
}

---
HLS modules:
ddr_read.c
#include "ap_cint.h"
#include "string.h"
#define MAXDATA 8192
void ddr_read (uint128 output[], volatile uint128 *ddr)
{
#pragma HLS INTERFACE m_axi port=ddr offset=direct max_write_burst_length=256
#pragma HLS INTERFACE axis port=output
int i, j;
uint128 buff_rd [MAXDATA];
memcpy(buff_rd, (uint128*)ddr, MAXDATA*sizeof(uint128));
for (i = 0, j=0; i< MAXDATA; i++, j+= 2) {
#pragma HLS PIPELINE
 output[j] = buff_rd[i];
 output[j+1] = buff_rd[i];
}
return;
}
- FICSES requires that each packet sent over AURORA should be 2 cycles (@100MHz)
- If the HLS output is directly sent to FICSES, you should make sure that each data is sent over 2 cycles. Otherwise, the data will be invalid!
- To respect this requirement, in this example the same data is outputted twice.

---
Testing
- Example designs that allow users to perform DDR access and check for both MARK1 and MARK2, as well as sw4x4 and sw5x5, is provided under:
  /home/asap/fic/FICSES/
- The directory structure is as follows:
//MK1 Vivado projects
//MK2 Vivado projects
//FICSES user programs

---
Testing
- The usual control from RaspberryPi is preserved.
- From Zeus (through FICSES) users can access any FIC board (MARK1 and MARK2) connected to the ring:
  - Start and reset HLS module
    - Through the control channel (Ch1)
  - Write/read a control register in func4x4/func5x5 on each board
    - Through the control channel (Ch1)
  - Setup routing table
    - Through the control channel(Ch1)
  - Write/read data to/from DDR
    - Through the data channel (Ch2)

---
Testing:
./host
- The “host” directory contains the following:
  - fpga_prog.sh: download bitsream to all 8 boards (by nyacom)
  - ficses.h: header file for FICSES control
  - main.c: User program

---
Testing:
ficses.h
- ficses.h contains the following fuctions:
  - int ficses_write_128KB(char* binary_file, int ficses_channel)
  - int ficses_read_128KB(char* binary_file, int ficses_channel, int * read_data)
    - int read_binary_file (char* binary_file, int * read_data)
    - int ficses_start(int channel_enable)
  - int ficses_register_access(int BOARD_ID, int command, int address, int payload, int ficses_channel, int * read_data)
    - int ficses_register_read(int BOARD_ID, int address, int ficses_channel)
    - int ficses_register_write(int BOARD_ID, int address, int payload, int ficses_channel)
    - int ficses_ap_start(int BOARD_ID, int ficses_channel)
    - int ficses_ap_rst(int BOARD_ID, int ficses_channel)
  - int ficses_table_setting(int BOARD_ID, char* table_file, int ficses_channel)
  - int user_write_data(float *array, int BOARD_ID, int data_count, int ficses_channel) (Customizable)

---
Testing:
main.c (example)

---
Remarks
- You must login as root in order to execute the different functions in ficses.h
- The board IDs should be always selected as (odd-even-odd-even-..)
- To broadcast a write command to a register, use 0xBB as the destination boards.
  (Read broadcast is not supported at the moment!!)